## Slide 1: Wellbore Stability
1.12-1
Notes: This is an introduction to wellbore stability.

## Slide 2: Failure Modes
Tensile Failure
Shear Failure
Matrix/Pore Collapse
Notes: Tensile failure: This occurs if the maximum tensile stress acting around a wellbore exceeds the
tensile strength of the formation. Two types of tensile failure can occur. The first is associated
with increasing the wellbore pressure and generating an hydraulic fracture (lost circulation
situation). The second type of tensile failure is extensional, where concentric failure surfaces can
develop around the wellbore if the pressure in the wellbore is reduced and/or if there are
significant seepage forces due to inflow. This means that material can spall into the wellbore or
can be “pushed or dragged” into the wellbore by flowing formation fluids, in an environment
where frictional resistance is reduced because there are no compressive stresses acting (the radial
effective stresses, at least, are tensile).
Shear failure: In a frictional material, shear failure is governed by the mean stress (arithmetic
average of the principal stresses), the deviatoric stress tensor (representation of the differences in
magnitudes of the in-situ principal stresses) and the shear characteristics of the medium (often a
Mohr-Coulomb failure envelope, where the governing material parameters are the cohesion - the
inherent shear strength - and the angle of internal friction). Shear failure can occur in an active
or a passive mode.
Matrix/Pore Collapse: This is structural collapse. It is governed by the spherical stress tensor
(stress average) and the matrix isostatic compressive strength (strength under hydrostatic stress
application). This failure is associated with a volume reduction and densification of the medium.

## Slide 3: Symptoms
The wellbore may slough because
Initiation and/or extension of hydraulic fractures
Local mobilization of pre-existing faults.
Sudden spalling may occur during swabbing or tripping.
Drag forces may cause rapid sand production.
Ductile formations such as salt, other evaporites and soft shales can squeeze and restrict the hole.
Certain shales can swell.
Notes: The rig crew may not be able to determine the cause of wellbore failure or wellbore stability, but there are a number of symptoms that stability problems are occurring. They are listed above.

## Slide 4: Shale Stability
Can be effected by:
  Exposure time
  Filtrate chemistry
  Ionic transport
  Dehydration (during UBD)
Notes: Some shales present additional problems from chemical instability. It is related fundamentally to inadequate mud weight and to the influx of water into the formation, which aggravates instability by increasing the near-wellbore pore pressure and by decreasing shale strength.

## Slide 5: Shale Stability
The two most relevant mechanisms are:
  the hydraulic pressure difference between the wellbore pressure and the shale pore fluid pressure
  Chemical potential differences between the drilling and shale pore fluids.

## Slide 6: Smectitic Shales
Ductile and creep
Reduced wellbore pressure accelerates creep
Chemically sensitive to mud filtrate’s ionic strength
Imbibition can occur with subsequent swelling, and shoughing

## Slide 7: Smectitic Shales
Salt, gilsonite or polymers can be added to the mud to stabilize these types of shales.

## Slide 8: Illitic Shales
Higher quartz content and usually more stable that Smectitic shales
Frequently more brittle and inert.
However, massive failure can occur during high pressure drawdown due to the brittleness and stored energy within the pore fluids.

## Slide 9: Failure Criteria
Von Mises
Tresca
Mohr-Coulomb
Druker-Prager
Hoek and Brown
Notes: Stability analysis is performed by determining the far-field principal stresses (using whatever methodology is available) calculating the stresses which exists around the wellbore due to this stress field and then then comparing the existing stresses with a failure criterion (representing the strength of the material at particular in-situ stress conditions). If the stress field concentrated around the wellbore exceeds the failure criterion, yield can occur.
It is necessary to define a failure criterion in order to analyze shear failure conditions. This slide lists five criteria. It is important to choose one that represents the characteristics of the medium in question. The Mohr-Coulomb is probably the simplest to use.

## Slide 10: Mohr-Coulomb
co + ntan 
  ......... shear stress (one-half of the difference between the maximum, and minimum principal stresses)
  n...... effective normal stress (average of the maximum and minimum effective principal stresses)
  co........ cohesion (intercept on a - nplot), and,
  ......... angle of internal friction (angle of Mohr-Coulomb locus from the naxis on a - nplot).
Notes: The basis of this relationship is that a failure locus is developed from laboratory triaxial testing. The yield or failure stress is characterized by the above equation. If the in-situ stress conditions are on or above this line (on a plot of shear stress versus normal stress) failure is predicted.

## Slide 11: Minimum Tolerable Pressures
Notes: A computational approach was used to develop the above Figure. It is an example of tolerable pressures to avoid shear failure, based strictly on linear elastic analysis (using Wang and Dusseault’s formulations). The reservoir simulated was assumed to have a depth of 5000 feet, HMAX = 4000 psi, HMIN varied, po = 2165 psi (0.433 psi/ft), = 35, and = 0.25. The cohesion varied. The figure indicates that cohesion is a dominant parameter and every effort should be made to determine it. It also shows differences between permeable and impermeable reservoirs. Wellbore pressures below the predicted value (psa) indicate instability in shear.